## Slide 1: Checkin 32
Virtual memory simplifies the task of the loader. What extra steps does the loader need to take without virtual memory?

## Slide 2: Machine Code Optimization
University of Kansas| Drew Davidson

## Slide 3: Previously Post-compilation toolchain
Compiler Toolchains
Overview
What GCC Does
Component Walkthrough
Assembler
Linker
Loader

## Slide 4
4
COMPILER
Regular
Languages
Syntactic
Definition
Lexical Analysis
Parsing
Syntax-Dir
Translation
Optimization
Semantic Analysis
Machine Codegen
Intermediate Representation
Code Generation
Postcompilation
Pit-stop

## Slide 5: Compiler Construction Progress Pics
Scanner
Lexical analysis
Parser
Syntactic analysis
Semantic analysis
Intermediate code generation
IR optimization
Final Code generation
Final code optimization
Source
Code
Finished
A naïve workflow from source code to target code
To-Do
Clean up some of the corners we cut
We’ve focused on correctness over efficiency, let’s try to win back some efficiency

## Slide 6: Today’s Outline Machine Code Optimization
Overview
Improving data allocation
Register allocation
Improving Final Code
Peephole optimization
Instruction Pipelines
Optimization

## Slide 7: Working With the Architecture Machine Code Optimization
Good machine code should:
Play to the strengths of the hardware
Compensate for weaknesses of the hardware
Such operations depend on specifics of the architecture

## Slide 8: Disclaimer: This is a Deep Area Machine Code Optimization
We hardly scratch the surface of compiler optimizations
There are more categories of machine-code optimization than we’ll cover
There are more optimizations within the categories we do cover
The tip of the iceberg

## Slide 9: Today’s Outline Machine Code Optimization
Overview
Improving data allocation
Register allocation
Improving Final Code
Peephole optimization
Instruction Pipelines
Optimization

## Slide 10: Sizing Activation Records Machine Code Optimization: Data Allocation
Easy mode: one AR slot for every temp, local, and arg
Source code
int foo(int a){ int v;
int r;
v = a-a*a;
r = v - 2;
}
3AC Code
enter foo
getarg 1, [a]
[t1] := [a] * [a]
[v] := [a] - [t1]
[r] := [v] - 2
foo AR
old RBP
old RIP
%rsp
%rbp
int r
int t1
int v
int a
Memory at Runtime
Surely one could use fewer memory slots!
Maybe we could
share some slots

## Slide 11: Liveness Machine Code Optimization: Data Allocation
A definition is live if it’s value is subsequently used
Insight: Variables can share space when they don’t interfere (i.e. aren’t simultaneously live)
We’ll capture the constraints via an abstraction called the interference graph
A := …
B := …
… := B
C := …
… := A
D := …
… := D
… := C
Use/Definition Sequence
Line_1
Line_2
Line_3
Line_4
Line_5
Line_6
Line_7
Line_8

## Slide 12: Liveness Machine Code Optimization: Data Allocation
The interference graph:
Nodes are variables
Edges show simultaneously live variables
A := …
B := …
… := B
C := …
… := A
D := …
… := D
… := C
Use/Definition Sequence
Line_1
Line_2
Line_3
Line_4
Line_5
Line_6
Line_7
Line_8
A
D
B
C
Interference Graph

## Slide 13: Liveness Machine Code Optimization: Data Allocation
Coloring:
Assign each storage location to a color
Color the interference graph so no nodes of the same color are adjacent
A := …
B := …
… := B
C := …
… := A
D := …
… := D
… := C
Use/Definition Sequence
Line_1
Line_2
Line_3
Line_4
Line_5
Line_6
Line_7
Line_8
A
D
B
C
Interference Graph
Loc2
Loc1
A
D
B
C

## Slide 14: Liveness Machine Code Optimization: Data Allocation
Allocation: Map all variables to their color’s location
Unfortunately, coloring is NP-Compete 
A := …
B := …
… := B
C := …
… := A
D := …
… := D
… := C
A
D
B
C
Interference Graph
Use/Definition Sequence
Loc2
Loc1
A
D
B
C
-24(%rbp) := …
-32(%rbp) := …
… := -32(%rbp)
-32(%rbp) := …
… := -24(%rbp)
-24(%rbp) := …
… := -24(%rbp)
… := -32(%rbp)
Allocation
Line_1
Line_2
Line_3
Line_4
Line_5
Line_6
Line_7
Line_8
foo AR
old RBP
old RIP
%rsp
%rbp
B / C
A / D
Memory at Runtime

## Slide 15: Today’s Outline Machine Code Optimization
Improving data allocation
Register allocation
Improving Final Code
Peephole optimization
Instruction Pipelines
Optimization

## Slide 16: Register Allocation Machine Code Optimization: Register Allocation
When possible, keep variables entirely in registers
Why?
Some computation requires register operands
Register operands are intrinsically faster
Register coloring
Assign a color to each available register
Optimal assignment is NP-Complete 

## Slide 17: Problem: Callee clobbers registers! Machine Code Optimization: Register Allocation
enter foo
[f1] := 2
[f2] := 3
call bar
[f3] := [f2] + [f1]
leave foo
enter bar
[b1] := 9
[b2] := 7
[glb_g] := [b1] - [b2]
leave foo
foo: pushq %rbp
movq %rsp, %rbp
addq $16, %rbp
movq $2, %r9
movq $3, %r10
callq bar
addq %r9, %r10
popq %rbp
retq
bar: pushq %rbp
movq %rsp, %rbp
addq $16, %rbp
movq $9, %r9
movq $7, %r10
subq %r10, %r9
movq %r9, (glb_g)
popq %rbp
retq
bar AR
old rip
old rbp
…
…
0x7fc0
…
old rip
old rbp
foo AR
r9
r10
rsp
rbp
0x7FA0
0x7FA8
0x7FB0
0x7FB8
0x7FB0
0x7FC0
0x7FA0
2
3
2
old rip
old rbp
…
…
free
foo AR
r9
r10
rsp
rbp
0x7FA0
0x7FA8
0x7FB0
0x7FB8
0x7FC0
0x7FC0
0x7FB0
2
3
1
free
old rip
old rbp
…
…
foo AR
r9
r10
rsp
rbp
0x7FA0
0x7FA8
0x7FB0
0x7FB8
0x7FC0
0x7FC0
0x7FB0
9
7
4
%r9
%r10
%r9
%r10
bar AR
old rip
old rbp
old rip
old rbp
foo AR
r9
r10
rsp
rbp
0x7FA0
0x7FA8
0x7FB0
0x7FB8
0x7FB0
0x7FC0
0x7FA0
9
7
3
2
3
1
4

## Slide 18: Which Registers To Use? Machine Code Optimization: Register Allocation
Register Allocation Complication:
Callees overwriting registers
Callees can’t statically learn which registers the caller is using
foo
bar
baz
Needs 2
registers
Needs 3
registers
Needs 2
registers
%r11, %r12, %r13, %r14, %r15
Assume these general purpose registers
%r11
%r12
%r11
%r12
%r13
%r14
%r15

## Slide 19: Register Conventions Machine Code Optimization: Register Conventions
Calling convention indicates which registers should be preserved across calls
Preserved (callee-saved): rbx, rsp, rbp, r12, r13, r14, r15
Volatile (caller-saved): rax, rdi, rsi, rdx, rcx, r8, r9, r10, r11

## Slide 20: Preserving Register Values Machine Code Optimization: Register Conventions
Analogy: housesharing
Imagine a function call. There’s a caller and a callee. Let’s use an analogy
Me (homeowner): caller
You (guest): callee
Function call: you stay at my house. Rooms: registers
Common rooms: you can goof around in there (volatile)
Restricted rooms: don’t touch anything (preserved)

## Slide 21: Preserving Register Values Machine Code Optimization: Register Conventions
Analogy: housesharing
Imagine a function call. There’s a caller and a callee. Let’s use an analogy
Me (homeowner): caller
You (guest): callee
Function call: you stay at my house. Rooms: registers
Common rooms: you can goof around in there (volatile)
Restricted rooms: don’t touch anything (preserved)
%r08
0x12
%r09
0xFF
%r10
0x97
%r11
0x13
%r12
0xF3
%r13
0x1111111111
volatile
preserved

## Slide 22: Preserving Register Values Machine Code Optimization: Register Conventions
Respectful housesharing
In the call
- You only touch the volatile registers
After the caller
- I don’t care
%r08
0x12
%r09
0xFF
%r10
0x97
%r11
0x13
%r12
0xF3
%r13
0x1111111111
volatile
preserved
0x32
0x19
Allowed
Caller code
movq $0x13, %r11
movq $0x12, %r08
callq
addq $1, %r11
movq $0, %r08
I can count on
%r11’s being same
I cannot count on
%r08’s value

## Slide 23: Preserving Register Values Machine Code Optimization: Register Conventions
Respectful housesharing
In the call
- You only touch the volatile registers
After the caller
- I don’t care
%r08
0x12
%r09
0xFF
%r10
0x97
%r11
0x13
%r12
0xF3
%r13
0x1111111111
volatile
preserved
Disrespectful housesharing
In the call
- You (also) touch the preserved registers
After the caller
- Caller’s expectation violated!!
0x32
0x19
0x88
Allowed
Illegal
(violated System V ABI)
Caller code
movq $0x13, %r11
movq $0x12, %r08
callq
addq $1, %r11
movq $0, %r08

## Slide 24: Preserving Register Values Machine Code Optimization: Register Conventions
Respectful housesharing
In the call
- You only touch the volatile registers
After the caller
- I don’t care
%r08
0x12
%r09
0xFF
%r10
0x97
%r11
0x13
%r12
0xF3
%r13
0x1111111111
volatile
preserved
Disrespectful housesharing
In the call
- You (also) touch the preserved registers
After the caller
- Caller’s expectation violated!!
0x32
0x19
0x88
0x13
Allowed
Sneaky housesharing
In the call
You (also) touch the preserved registers
You restore the preserved values before return
After the caller
The caller never knows of your deviance
Illegal
(violated System V ABI)
Allowed

## Slide 25: Implementing Register Conventions Machine Code Optimization: Register Conventions
Using callee-saved registers
Being a “sneaky guest”
Push the preserved register values before you use them
Pop the stacked values before you return
Prologue
pushq %rbp
movq %rsp, %rbp
addq $16, %rbp
pushq %r08
pushq %r09
subq $32, %rsp
Epilogue
addq $32, %rsp
popq %r09
popq %r08
popq %rbp
retq
Using caller-saved registers
Being a “sneaky owner”
Save a volatile register to the stack
Pop the stacked values before you return
Call site
pushq %r11
pushq %r12
callq fn_callee
popq %r12
popq %r11

## Slide 26: Today’s Outline Machine Code Optimization
Improving data allocation
Register allocation
Improving Final Code
Peephole optimization
Instruction Pipelines
Optimization

## Slide 27: Fixing “Obviously Sub-Optimal” Code Machine Code Optimization: Peephole Optimizations
A code generator may output obviously “weak” code
why?
  Ignoring global context
  Correctness-first design
Solution: pattern-match the most obvious problems
An obvious flaw

## Slide 28: The Idea of the Peephole Machine Code Optimization: Peephole Optimizations
Called “peephole” optimization because we are conceptually sliding a small window over the code, looking for small patterns

## Slide 29: Remove Semantic No-ops Machine Code Optimization: Peephole Optimizations
Remove semantic no-op sequences
Push followed by pop
Add/sub 0
Mul/div 1
subq $8, %rsp
movq %r10, (%rsp)
movq (%rsp), %r10
addq $8, %rsp
push
pop
addq $0 %rax
imulq $1 %rbx

## Slide 30: Sequence Simplification Machine Code Optimization: Peephole Optimizations
Store then load
Arithmetic equivalence
Jump to next
movq %rax, -8(%rbp)
movq -8(%rbp) %rax
Useless instruction
addq $1 %r11
addq $2 %r11
Just add 3
jmp Label1
Label1: addq $2, %rax
Useless instruction

## Slide 31: Instruction Strength Reduction Machine Code Optimization: Peephole Optimizations
Instruction Strength Reduction
Prefer “weak” (narrow/specialized instruction) instead
Avoid “strong” (general-purpose) instruction
imulq $2 %rax
shift-left %rax
addq $1 %rax
inc %rax
Requires knowledge of the fast and
slow instructions
“Weaker” is better

## Slide 32: Peephole Optimization: Summary Machine Code Optimization: Peephole Optimizations
Concept
Final code “postprocessing”
Slide a window over the program that pattern-matches suboptimal cases
Benefits
Remove some consequences of naïve machine code generation
Leverage hardware features
  Faster instructions

## Slide 33: Today’s Outline Machine Code Optimization
Improving data allocation
Register allocation
Improving Final Code
Peephole optimization
Instruction Pipelines
Optimization

## Slide 34: Background: Multi-stage Cycles Machine Code Optimization: Delay Slots – Branch Hazards
The classic cycle of a processor:
Fetch - read value at the program counter
Decode – figure out what the instruction is
Execute – do what the instruction
Write-back – commit the results to register/memory
If we did all of this sequentially, we’d waste time & resources

## Slide 35: Background: Instruction Pipelines Machine Code Optimization: Delay Slots – Branch Hazards
Idea: Start on next instruction before current done
Time
t0
Time
t1
Time
t2
Time
t3
Time
t4
Time
t5
Time
t6
Time
t7
Time
t8
I1: addq %rax %rbx
I2 : subq %rcx %rdx
I1
Fetch
I1
Decode
I1
Execute
I1
Write
I2
Fetch
I2
Decode
I2
Execute
I2
Write

## Slide 36: Background: Instruction Pipelines Machine Code Optimization: Delay Slots – Branch Hazards
Idea: Start on next instruction before current done
Instr
Fetch
Instr
Decode
Execute
Writeback
Time
t0
Time
t1
Time
t2
Time
t3
Time
t4
Time
t5
Time
t6
Time
t7
Time
t8
I1: addq %rax %rbx
I2 : subq %rcx %rdx
I1
Fetch
I1
Decode
I1
Execute
I1
Write
I2
Fetch
I2
Decode
I2
Execute
I2
Write

## Slide 37: Background: Instruction Pipelines Machine Code Optimization: Delay Slots – Branch Hazards
Idea: Start on next instruction before current done
Instr
Fetch
Instr
Decode
Execute
Writeback
Time
t0
Time
t1
Time
t2
Time
t3
Time
t4
Time
t5
Time
t6
Time
t7
Time
t8
I1: addq %rax %rbx
I2 : subq %rcx %rdx
I1
I1
I1
I1
I2
I2
I2
I2
Tremendous
Savings!
addq %rax, %rbx
addq %rbx, %rcx
addq %rdx, %r11
addq %rax, %rbx
addq %rbx, %rcx
addq %rdx, %r11

## Slide 38: Lecture End! Machine Code Optimization: Wrap-Up
Summary:
Be careful about which instructions you use
Selection: the choice of instructions in output
Scheduling: the order of instructions in output
Next Time:
Optimizing program structure