## Slide 1: Checkin 23
Rather than using bit-addressable or word-addressable (16-bit) memory, X64 uses byte addressable memory. Why?

## Slide 2: Administrivia Announcements

## Slide 3: x64 Basics
University of Kansas | Drew Davidson

## Slide 4: Last Lecture Encoding Programs
Representing Whole Programs in Hardware
Data
Code
ISAs
X64 – Example target
Architecture
What you should know:
ISA concept
That data and code share memory
  The instruction pointer
How to play with ASM code

## Slide 5: Recall: Instructions Review x64 Intro
.text
.globl _start
_start:
movq $60, %rax # Choose syscall exit
movq $4, %rdi # Set syscall arg - return code
syscall
We’ve already seen two instructions:
movq <o1> <o2>
  Move quadword in o1 into quadword o2
syscall
  Invoke a system service
Flow of data

## Slide 6: Recall: x64 Registers Review x64 Intro
Name | Number | “Nickname”
%rax | 0 | Accumulator
%rbx | 1 | Base
%rcx | 2 | Counter
%rdx | 3 | I/O
%rsi | 4 | String source
%rdi | 5 | String destination
%rbp | 6 | Base pointer
%rsp | 7 | Stack pointer
%r08 – %r15 | 8 - 15 | General purpose
%rip | - | Instruction pointer
%rflags | - | Status flags
Computation needs to be done on registers
General workflow:
src code
a = b <opr> c
asm code
Load b into a register
Load c into another register
Do opr on registers
Store result register into a
General purpose
For our needs
Inaccessible as
regular operands
Used for bookkeeping
Bonus general purpose for us

## Slide 7
X64 Discussion
Some perspective
Architecture Details
Basic operators
Memory Directives
Architecture
Today’s Lecture X64 Basics

## Slide 8: ASM Instruction Syntax Lecture Outline –Writing x64
As with everything x86-related, it’s complicated
We’ll use the AT&T Syntax:
  <opcode><sizesuffix> <src operand(s)> <dst operand>
Immediates (i.e. constant values) prefixed by $
Registers prefixed by %
Memory lookup (i.e. dereference) in parens
movq $5, (%rax)
mov the 64-bit value 5 into the 64-bit
memory address specified by register rax

## Slide 9: Directives Lecture Outline –Writing x64
Indicates a command to the assembler
  Layout, program entrypoint, etc.
Example:
.globl X
Indicates that symbol X is visible outside of the file

## Slide 10: Segment Directives Lecture Outline –Writing x64
.data
Lay out items in the data segment
.text
Lay out items in the user text segment
Instructions go here
Globals go here

## Slide 11: Labels Lecture Outline –Writing x64
The assembler allows us to specify “placeholder” addresses that will be used later
  Translated to “real” addresses by a utility called the linker
Valid for both data and code locations
jmp 0x12d34a5678a
jmp LBL1
…
LBL1: movq $5 (%rax)

## Slide 12: System Calls Lecture Outline –Writing x64
To interact outside program memory, need the help of the OS
%rax # Which system call (60 is exit)
%rdi # Set syscall arg – (exit takes the return code)
syscall

## Slide 13: Time to put it all together! Lecture Outline –Writing x64
Photo Credit: Tim Klein - https://puzzlemontage.crevado.com

## Slide 14: A Complete Program Lecture Outline –Writing x64
.text
.globl _start _start: movq $60, %rax # Choose syscall exit movq $4, %rdi # Set syscall arg - return code
syscall

## Slide 15: Actually Running a Program Lecture Outline –Writing x64
Invoking the assembler and linker
as –o start.o start.s
ld start.o –o prog
./prog
echo $?

## Slide 16: Reviewing ISAs ISAs
ISAs
Provide an interface from software to hardware
We’ll target assembly code, assembler will take it from there
X64
A popular architecture
We’ve covered the basic instruction format and a simple program

## Slide 17: Compiler Construction Progress Pics
Scanner
Lexical analysis
Parser
Syntactic analysis
Semantic analysis
Intermediate code generation
Final Code generation
Output code in T
Source code (sequence of chars)
Done:
Validated and abstracted input program
Flattened the input program to a linear representation
ToDo:
Concretize to the target architecture
We gotta
understand
this!
In progress
Done!
Done!
Done!
Done!

## Slide 18: A Moment of Appreciation x64 Basics: Perspective
We’re writing real-deal x64 - no special tools needed
Our x64 code looks (mostly) like what comes out of gcc
gcc –S prog.c –o prog.s
gcc –c prog.s –o prog.o
gcc prog.o –o prog.exe
Unfortunately for clarity, there are a lot of extra directives we might want to strip:
gcc -fno-asynchronous-unwind-tables -fno-dwarf2-cfi-asm -O0 -S blah.c -o blah.nodebug.S

## Slide 19: Docs: A Benefit to x64’s Popularity x64 Basics: Perspective
Lots of good, thorough documentation out there
Some best used as reference rather than walkthrough
4922
Pages!
https://software.intel.com/sites/default/files/managed/39/c5/325462-sdm-vol-1-2abcd-3abcd.pdf

## Slide 20: There are a LOT of Instructions in X64! X64 Basics: Perspective

## Slide 21: Keeping to the “Easy” Path X64 Basics: Perspective
Like 15
opcodes
665
The rest of x86
We’ll sidestep most of the x64 complexity
We’ll just stick to those instructions we need
Give you the pointers to explore the rest of the ISA

## Slide 22
X64 Discussion
Some perspective
Architecture Details
Basic operators
Memory Directives
Architecture
Today’s Lecture X64 Basics

## Slide 23: Let’s Dive In to X64! X64 Basics – Architecture Details
X64

## Slide 24: Simple Arithmetic Instructions x64 Basics
negq <o1>
addq <o1> <o2>
subq <o1> <o2>
o1 = -o1
Example
movq $4, %rax
negq %rax
Example
movq $4, %rax
movq $5, %rbx
addq %rax, %rbx
Example
movq $4, %rax
movq $5, %rbx
subq %rax, %rbx
o2 = o2 + o1
o2 = o2 - o1
At this pt:
%rbx = 9
At this pt:
%rbx = 1
At this pt:
%rax = -4
“Main”
operand
“Support”
operand
Take <o2> and “do” <o1> to it

## Slide 25: Wacky Arithmetic Instructions x64 Basics
imulq <o1>
idivq <o1>
Example
movq $2, %rax
movq $4, %r11
imulq %r11
Example
movq $0, %rdx
movq $6, %rax
movq $2, %r8
idivq %r8
%rax = %rdx:%rax / o1
%rdx = %rdx:%rax % o1
%rdx:%rax = %rax * o1
At this pt:
%rax = 8
%rdx = 0
At this pt:
%rax = 3
%rdx = 0
2 * 4
6 / 2

## Slide 26: Logical Instructions x64 Basics
notq <o1>
andq <o1> <o2>
Example
movq $1, %rcx
notq %rcx
Example
movq $12, %rdx
movq $10, %rax
andq %rax, %rdx
o1 = bitflip o1
o2 = o2 & o1
orq <o1> <o2>
o2 = o2 | o1
Example
movq $12, %rdx
movq $10, %rax
orq %rax, %rdx
xorq <o1> <o2>
o2 = o1 ^ o2
Example
movq $5, %rdx
movq $6, %rax
xorq %rax, %rdx
At this pt:
%rcx = -2
At this pt:
%rdx = 8
At this pt:
%rdx = 14
At this pt:
%rdx = 3
%rdx 0..1100
%rcx 1..10
0..01
0..10
Why -2?
Before and
After bitflip
2’s complement…
Flip all bits
Add 1
0 + 2 + 0 = (negative) 2
%rcx 0..01
%rax 0..1010
%rax 0..1000
Before bitflip
After and
0 + 8 + 0 + 0 + 0 = 8
%rdx 0..1100
Before or
%rax 0..1010
%rax 0..1110
After or
0 + 8 + 4 + 2 + 0 = 14
%rdx 0..0101
Before xor
%rax 0..0110
%rax 0..0011
After xor
0 + 2 + 1 = 3

## Slide 27: Conditionals x64 Basics
Another weird x86 thing
conditional jump instructions – no explicit condition!
Uses the flags register rflags
  Assumes a previous operation has set the flags register
je <LBL>
Jump to label LBL if equal, else fallthrough
“Wait… jump if what is equal?”
cmpq %rax, %rbx
je <LBL>
Jump to label LBL if rax and rbx are equal,
else fallthrough
movq $1, %rbx
movq $1, %rax
cmpq %rax, %rbx
je LBL_1
Jump to LBL_1

## Slide 28: Conditionals and rflags x64 Basics
OF “Overflow Flag”
SF “Sign Flag”
ZF “Zero Flag”
Result exceeds storage
Result was negative
Result was zero
cmpq src1 src2 : Set flags as though computing src2 – src1
E
(E)quality
ZF
NE
(N)ot (E)qual
ZF
G
(G)reater
(ZF ) OF
L
(L)ess
OF
GE
(G)reater or (E)qual
F OF
LE
(L)ess or (E)qual
(SFOF) ZF
rflags: bitvector register of conditions
sete
setne
setg
setl
setge
setle
je
jne
jg
jl
jge
jle
movq $1, %rax
movq $2, %rbx
cmpq %rax, %rbx
sete <o1>
At this pt:
<o1> = 0
sete %rax
sete %al

## Slide 29: You can now (kinda) write assembly programs! x64 Basics
GCC
.globl _start
.text
_start:
movq $1, %r10
movq $2, %r11
subq %r10, %r11
#exit
movq $60, %rax
movq %r11, %rdi
syscall
int main(){
return 2 – 1;
}
src code
asm code

## Slide 30
X64 Discussion
Some assurances
Architecture Details
Basic operators
Memory directives
Architecture
Today’s Lecture X64 Basics

## Slide 31: Manipulating Memory X64 Basics
Data can’t always fit into registers
Two things we need to do:
Allocate memory
Read/write memory
A different kind of memory being
manipulated

## Slide 32: Recall: Memory as an Array X64 Basics
Memory is just a big ol’ array of bytes (with OS mediation)
Assembler and friends will map the code into memory
We still need to map data to memory
  variables, objects, strings, arrays, etc.
0x40008D
0x00
0x00
0x00
Address
Address
Address
Address
0x07
0x40008C
0x40008E
0x40008F
data
The 32-bit value 7
Address
0x400086
0x40087
0x400088
0x400089
0x40008A
0x4d
0xe9
Address
Address
Address
Address
Address
0x4c
0x89
0xef
0x25
0x40008B
code
subq %r12, %r13
movq %r13, %rdi
Lbl1: subq %r12, %r13
0x400086: 0x4d 0xe9 0x25
Lbl2: movq %r13, %rdi
0x400089: 0x4c 0x89 0xef
Assembly code
Binary memory
0x40008C: 0x7
????????????????

## Slide 33: Lecture Done! x64 Basics: Summary
Some basic x64 details
Instructions
Data directives
Memory intuition
Next Time
Dive further into x64
Describe memory operations